## Slide 1: ESRC OEE Start Up
As of 5/25/18
What does the following mean on the Laser?
  RUN: Producing wire (cut and laser)
  OTHER (UNPLANNED SETUP):
    Wire type change for ASL
    Operator Pause Operation
  IDLE: everything else
  TIE-IN (Planned Downtime): scheduled between shift change
  LUNCH (Planned Downtime): operator lunch
  BREAKS (Planned Downtime): operator breaks
  PLANNED SETUP:
    Group Code Change
    Effectivity Change
    Bundle No Change
Red = new tag line

## Slide 2: Tag lines provided by Spectrum 6/6/19 Group Code Change
Group code change (UP1) notification box pop-up to operator acknowledgement, and
UP1A [User Prompt Displayed Group] 38909.7704492 10:48:29 {15.5928}
UP1B [User Prompt Cleared] 38912.349479 10:48:32 {2579.0298}
Labeled: IDLE (Group Code Change)

## Slide 3: Tag lines provided by Spectrum 6/6/19 Effectivity Change
Effectivity Change (UP2)
UP2A [User Prompt Displayed Effectivity] 38912.349479 10:48:32 {0}
UP2B [User Prompt Cleared] 38913.2952102 10:48:33 {945.7312}
Labeled: IDLE (Eff Change)

## Slide 4: Tag lines provided by Spectrum 6/6/19 Bundle No Change
Bundle No Change (UP3)
UP3A [User Prompt Displayed Bundle No] 38913.2952102 10:48:33 {0}
UP3B [User Prompt Cleared] 38913.9921564 10:48:33 {696.9462}
Labeled: IDLE (Bundle No. Change)

## Slide 5: Tag lines provided by Spectrum 6/6/19 Operator Pause
Operator pause selection to unpausing
PA1A [User Pause Start] “date/time number” “time” “{}
and
PA1B [User Pause Stop] “date/time number” “time” “{}
Labeled: IDLE (Pause)

## Slide 6: Tag lines provided by Spectrum 6/6/19 Operator Logged into Laser
User domain id tracking on what operator is logged into the laser
Please search for the following tags in the communications log (should be at the start of a new file):
"/// SOFTWARE STARTUP \\\" "Computer Name: " "User Name : " "OS Full Name : " "OS Version : "
You should see the PC name and Windows user login name.